Displaying The Windows of the 2001

Under normal usage of the 2001, a user would use the :SENSE:DATA? to return 
a reading from the 2001. Using this command only returns the data in the 
primary window. It does not return the units nor does it return any of the 
information from the secondary display. If a programmer chooses to return 
the data from the secondary window, he or she would have to program the 2001 
to measure the very specific paramters. For example, if the 2001 is set for 
DC volts and the next button was pushed, the display may look as follows:

+064.8283  mVDC
+000.405  mVAC           +060.15      Hz

In this case, only the value +64.8283E-03 would be returned to the computer.

To return the entire display, the command :DISPLAY:WINDOW1:DATA? is sent to 
the 2001 to return the first window display and :DISPLAY:WINDOW2:DATA? is 
sent to return the second window display. As shown in the example program 
below, both windows can be returned:

If meter_enabled Then
    cmd$=":DISPLAY:WINDOW1:DATA?"
    Call Send(GPIBAddress,cmd$,status%)
    If status% = 0 Then
	Call Enter(disp1$, 21, l%, GPIBAddress, status%)
	If status% = 0 Then
	    cmd$=":DISPLAY:WINDOW2:DATA?"
	    Call Send(GPIBAddress,cmd$,status%)
	    If status% = 0 Then
		Call Enter(disp2$, 33, l%, GPIBAddress, status%)
		If status% = 0 Then
		    Print disp1$
		    Print disp2$
		End If
	    End If
	End If
    End If
End if

Please note in each Call Enter commands the values 21 and 33. The top 
window of the 2001 can display 20 characters and the bottom window can 
display 32 characters. When the window string is returned to the host 
computer, all 20 and 32 characters are returned along with an additional 
line feed (LF) character. Thus, to properly transfer the entire window 
string, 21 and 33 characters must be returned, otherwise, an error condition 
will occur. When both window strings have been transferred, the information 
can be displayed on the CRT or an application program can separately parse 
the information for the numerical data only for future use.

John Tucker   5/1/92